## Slide 1
Setup 3 (Drill-2, drill bit#-6)
Setup 2 (Drill-1, drill bit-2)
Current Technology: Automatic drilling
Material detection
(ML)
Drilling session
Concrete
Setup 1
Specialized
Controller
Iron bars
Setup 1
Specialized
Controller
AD10
actions
Setup 1 (Drill-1, drill bit-1)
Notes: A proposed plan for a presentation would be as follow;
Today we have an automatic drillcontrol, albeit a naive version, which depends on specialized controllers for each setup of the drill (Drill setup includes: drill type, drill bit, stand, angle of drilling).
This all is based on material detection and a new setup controller would be needed to drill with the current setup.
Material detection is a developed machine learning (ML) algorithm, which using data from sensors during drilling sessions and could classify the drilled material in real time.
For each material and setup specialized controllers have to be developed. Such controllers will generate the feeder (AD10) actions (pushing down more/less, stop, retract).
This development could lead to a set of specialized controllers that varies a lot across different setups and require a lot from the driller.

## Slide 2
Automatic drilling effectiveness
Time
Depth
Air
Concrete
Iron bars
Expert drilling
Automatic drilling
Notes: The Specialized controllers will never be able to reach the performance of a professional driller as there is no learning in the controller part and it is static after a release.
An improved release of the algorithm could be developed for each setup over time, but this is time-consuming and tedious.

## Slide 3
Material detection
(ML)
Drilling session
AD10
actions
Reinforced Learning (RL) - based drilling
RL-based
controller
Notes: Instead we propose developing an entire framework that builds on a material detection algorithm, but it learns the controller part generically.
This makes sure that the control can learn general enough to take care of all possible drilling setups while simultaneously improve over time.

## Slide 4
RL-based drilling effectiveness
Time
Depth
Air
Concrete
Iron bars
Expert drilling
RL-based drilling
Notes: Since this setup improves over time, it will eventually perform better than an expert driller. Initially we start of the algorithm by training on drilling sessions performed by professional drillers, this to give the RL a head start.

## Slide 5
Material detection
(ML)
Collaborative ML controller
ML controller
Drilling site #2
Drilling site #3
Drilling site #1
On-site metadata
Cloud-based computation/storage
Updated ML algorithms
Notes: Over time, the algorithm will be so good that it should not only rely on general historical drilling knowledges, but rather it can acquire knowledge of the upcoming drilling session ahead of time by communicating to nearby drills.
Site specific information, like material characteristics, can be utilized by the machine to prepare how to best drill the current hole.

## Slide 6
Material detection
(ML)
Cutting session
Actions
Other machines
ML controller
Notes: Once the entire framework has been developed, the same setup could be applied to different kinds of machines, for instance cutters if they are mounted on a controllable support.